## Slide 1
SBX vs. Illumina: M2_GEX Platform Comparison
Cell Ranger vs. sbxpress (minimap2) | Illumina / SBX-P5 / SBX-P7 | CAT02 / ABRF

## Slide 2
1
Study Design
• One sample, M2_GEX, pulled from a 15-sample pooled NovaSeqX run (NovaSeqX Series, CE15204)
• Carried through 3 technical preparations:
  ‣ Illumina — standard sequencing
  ‣ SBX-P5 — Roche SBX, CB/UMI read first
  ‣ SBX-P7 — Roche SBX, cDNA read first
• × 2 analysis pipelines:
  ‣ Cell Ranger (10x Genomics, STAR-based)
  ‣ sbxpress — minimap2-based, splice-aware, same annotation/molecule/matrix/cell stages for all platforms
• = 6 conditions compared head-to-head on identical downstream logic (sbxpress audit) or native vendor pipeline (Cell Ranger metrics)
Caveat: single-sample deep dive — the other 14 pooled samples were demultiplexed only, not carried through this comparison (see Limitations).

## Slide 3
2
Read Architecture Sets Up Everything Downstream
 | Illumina R2 | SBX-P5 R2 | SBX-P7 R2
Length | fixed 90 bp | variable, mean 226 bp | variable, mean 244 bp
Max length | 90 bp | 649 bp | 649 bp
Read structure | short-read, STAR-tuned | long cDNA insert | long cDNA insert
• SBX reads carry 2.5–2.7× more sequence per read than Illumina R2
• This single fact drives the mapping-efficiency, depth-equivalence, and cost-parity results on the following slides

## Slide 4
3
Mapping Efficiency by Platform × Pipeline
 | Illumina/CR | Illumina/mm2 | P5/CR | P5/mm2 | P7/CR | P7/mm2
Unmapped | 3.08% | 19.81% | 9.27% | 6.78% | 7.41% | 1.37%
Gene-assigned | 55.08% | 58.16% | 63.82% | 58.25% | 66.13% | 60.26%
• sbxpress out-recovers Cell Ranger on SBX reads: lower unmapped %, more molecules counted overall
• sbxpress underperforms Cell Ranger on standard Illumina reads — minimap2 leaves ~5× more reads unmapped
• Interpretation: the aligner is presently tuned toward long SBX reads, not short 90bp Illumina R2 — not a general minimap2-vs-STAR verdict

## Slide 5
4
Cell Calling & Sensitivity
 | Illumina | SBX-P5 | SBX-P7
Reads | 2.81B | 1.31B | 1.16B
Cells called | 32,357 | 33,371 | 33,223
Median genes/cell | 2,777 | 2,307 | 2,414
Median UMI/cell | 4,663 | 4,046 | 4,270
Sequencing saturation | 77.8% | 61.3% | 56.6%
• Cell calls converge to nearly the same number (~32–33K) despite SBX using ~2.3× fewer reads
• Lower SBX saturation at matched cell count = library not yet sequenced to exhaustion — room to go deeper or reallocate reads elsewhere
Caveat: Q30-in-barcode/RNA/UMI reads 0.0% for SBX in Cell Ranger's own metrics — an artifact of a flat placeholder quality string in the synthetic FASTQ, not a real quality signal. Omit or footnote; do not present as an SBX quality problem.

## Slide 6
5
Read Depth for Equivalent Coverage
• Question: how much SBX sequencing is needed to match Illumina/Cell Ranger's molecule recovery (285.7M molecules, from 2.81B reads / 252.7 Gb of R2)?
• Modeled with a two-point Michaelis-Menten saturation fit per condition (full-depth + built-in 1/64 subsample point from each sbxpress audit)
To match Illumina's molecule recovery | Reads needed | vs. Illumina reads | Gb needed | vs. Illumina Gb
SBX-P7 / sbxpress | 1.12B | 39.8% | 272.8 Gb | 108.0%
SBX-P5 / sbxpress | 1.39B | 49.6% | 315.0 Gb | 124.7%
• Fewer reactions, not fewer bases: SBX needs 40–50% of Illumina's read count, but 108–125% of its Gb — state both units, they point opposite directions

## Slide 7
6
Cost-Parity Breakeven
• No external price data required — only the depth ratio from the previous slide
• Confirmed: both platforms are billed per run/lane, so $/read is the right lens (not $/Gb)
Billing unit | SBX-P7 breakeven price ratio | SBX-P5 breakeven price ratio
Per read/reaction (primary) | up to 2.51× Illumina's $/read | up to 2.01× Illumina's $/read
Per Gb output (secondary context) | at/below 92.6% of Illumina's $/Gb | at/below 80.2% of Illumina's $/Gb
SBX has real per-reaction pricing headroom (up to ~2×) under the confirmed per-run/lane billing model — this is the number to lead with.

## Slide 8
7
Pipeline Comparison: Cell Ranger vs. sbxpress
Condition | Cell Ranger molecules | sbxpress molecules | Δ
Illumina | 285.7M | 226.7M | −21% (sbxpress underperforms)
SBX-P5 | 264.6M | 281.6M | +6.4% (sbxpress ahead)
SBX-P7 | 277.2M | 296.7M | +7.0% (sbxpress ahead)
• sbxpress recovers ~6–7% more molecules than Cell Ranger on SBX data — a real, current advantage on the platform it's built for
• sbxpress recovers ~21% fewer molecules than Cell Ranger on standard Illumina reads — not yet a general-purpose replacement
• Read this as "tuned for long reads, not yet tuned for short reads" rather than "better" or "worse" in the abstract

## Slide 9
8
CB/UMI Position: A Yield/Fidelity Tradeoff
• Counter-intuitive result: P7 (cDNA read first) beats P5 (CB/UMI read first) on final molecule recovery — despite P5 protecting the barcode
Stage 1: raw signal → valid reads | SBX-P5 (CB/UMI first) | SBX-P7 (CB/UMI last)
Fully parsed | 62.6% | 46.9%
Unparseable | 13.9% | 33.8%
Barcode whitelist hit rate | 76.7% | 68.4%
Stage 2: alignment quality (surviving reads) | SBX-P5 | SBX-P7
Unmapped | 6.78% | 1.37%
Heavily-clipped | 1.22% | 0.28%
Gene-assigned | 58.25% | 60.26%
Molecules recovered | 281.6M | 296.7M
Working hypothesis: SBX signal quality decays over read position — whichever segment is decoded second is degraded. Barcode degradation is partially recoverable (whitelist correction); cDNA degradation is not — so protecting cDNA (P7) wins on final yield. Caveat: confirm P5/P7 = same library in both orientations, not the 10x 5′/3′-kit chemistry distinction, before presenting as a pure orientation effect.

## Slide 10
9
Read-Length Recovery: Short Reads Are Not the Weak Point
Length bin | P5 % of reads | P5 success% | P7 % of reads | P7 success%
75–99 bp | 2.6% | 60.6% | 0.3% | 61.8%
150–174 bp | 6.5% | 59.7% | 5.0% | 62.8%
200–224 bp | 15.9% (peak) | 60.9% | 17.6% (peak) | 62.8%
225–249 bp | 16.9% | 58.8% | 19.2% (peak) | 61.0%
250–274 bp | 14.3% | 56.9% | 16.1% | 59.1%
300–324 bp | 6.2% | 54.5% | 7.1% | 56.9%
450–474 bp | 0.12% | 53.9% | 0.14% | 57.1%
700–724 bp | 0.00% | 48.1% | 0.00% | 55.5%
• “Success%” = gene-called reads / total reads at that length. “% of reads” = share of the whole dataset in that bin — most reads sit in a narrow window
• P5: ~78% of reads fall in 150–299bp; P7: ~82%. The long tail where the P5-vs-P7 gap widens most (≥450bp) is under 0.3% of reads for both — a real, mechanistically interesting effect, but a small share of the total
• The P5-vs-P7 success gap still widens with length even in the well-populated zone: +1.2pp at 75–99bp → +2.2pp at 250–274bp → +7.4pp at 700–724bp
Read-level (gene-called/total), not molecule-level — no length attribution exists yet for deduplicated molecules. Illumina is fixed at 90bp (single bin, ~58.2% success, not shown here) — a sanity anchor, not a length trend. Unmapped-rate-by-length (below 250bp) is still not measured — this does not fully resolve the Fragment-Length Sweet Spot open question two slides ahead.

## Slide 11
10
Artifacts & Contamination (QC Check)
% of mapped reads (Cell Ranger BAMs) | Illumina | SBX-P5 | SBX-P7
Adapter | 0.040% | 0.202% | 0.122%
TSO | 9.529% | 5.691% | 8.079%
polyA (3′) | 0.154% | 0.067% | 0.124%
polyT (5′) | 0.017% | 0.220% | 0.021%
• All contamination classes stay under 10% across every condition — no platform shows a qualitatively different contamination profile
• Frame as a data-quality check that passed, not a headline comparison metric

## Slide 12
11
Fragment-Length Sweet Spot — Open Question
• SBX bills per run/lane, and reads/run is tunable by target molecule size — shorter molecule → more reads/run at fixed cost
• Real optimization target: useful molecules per run = reads_per_run(length) × P(read becomes a counted molecule | length)
• What we know (250–650 bp range only): gene-assignment specificity IMPROVES as length decreases — opposite of a naive “shorter reads map worse” assumption
• What's missing:
  ‣ reads-per-run vs. target-length function — a device/chemistry throughput property, not in any dataset reviewed
  ‣ mapping/unmapped behavior below 250bp — current analysis excludes unmapped reads by construction
Do not present a claimed optimum — state the shape of the problem and the two open curves needed to solve it.

## Slide 13
12
Limitations
• Single-sample deep dive: only M2_GEX was carried through this full comparison; 14 other pooled samples were demultiplexed only
• Q30-in-barcode/RNA/UMI reads 0.0% for SBX is a synthetic-FASTQ placeholder-quality artifact, not a real quality measurement
• Cost-parity numbers are ratios, not dollar figures — confirmed per-run/lane billing, but no absolute list price was available
• Fragment-length sweet spot is unresolved (previous slide)

## Slide 14
13
Conclusions & Recommendations
• SBX + sbxpress is a real, measured advantage on SBX's own data today: more molecules recovered than Cell Ranger, at 40–50% of Illumina's read depth for equivalent coverage, with real pricing headroom under per-run/lane billing
• sbxpress is not yet a drop-in replacement for the standard Illumina short-read path — that gap is expected and tracked separately (see mapping.md / mapping-evaluation validation work)
• P7 (cDNA read first) is the stronger SBX orientation on every downstream metric measured — recommend as default pending confirmation of the P5/P7-vs-chemistry caveat
• Next steps:
  ‣ Resolve the fragment-length throughput curve with device engineering data
  ‣ Extend this comparison beyond the single M2_GEX sample
  ‣ Get actual per-read/per-lane list prices to convert breakeven ratios into real dollar figures